MM SYSTEM CORPORATION

TRENCH & ACCESS COVERS SPECIFICATIONS

PART 1 — GENERAL

1.01 RELATED DOCUMENTS

A. Drawings and general provisions of the Contract, including General Conditions, Supplementary Conditions and Division-1 General Requirements, apply to the work of this section.

1.02 WORK INCLUDED

A. Furnish and install complete MM Systems Corporation trench grate systems.

1. Trench covers.

2. Access covers.

3. Trench Liners.

1.03 RELATED WORK

A. Related work which is specified elsewhere.

1. Concrete work: Section 03000.

2. Cast-in-place Concrete:  Section 03300.

3. Grout:  Section 03600.

1.04 REFERENCES

A. Publications listed herein are part of this specification to the extent referenced. The criteria established in the specifications shall take precedence over the standards referenced herein. (Three examples of reference standards are given below.)

1. American Society for Testing and Materials (ASTM):

- ASTM A 36, Standard Specification for Structural Steel

- ASTM B 209, Standard Specification for Aluminum and Aluminum-Alloy Sheet and Plate.

- ASTM B 221, Standard Specification for Aluminum and Aluminum-Alloy Extruded Bars, Rods, Wire, Shapes and Tubes.

1.05 DEFINITIONS

- Define industry and product terms as necessary.

1.06 SYSTEM DESCRIPTION

- [Trench covers] [Access covers] shall be [blockout] [cast-in-place] installation.

- [Trench covers shall cover the trench completely and] [Access covers] shall be flush with surrounding finish floor surfaces to allow unrestricted pedestrian traffic.

- Allowable load on [trench covers] [access covers] shall be [__________psf uniform load and/or __________lbs. concentrated load] (see load chart in catalog) with no more than [1/16] [1/8] [1/4] inch deflection.  In the absence of load selections, allowable load on [trench cover] [access cover] shall be 200 psf (or 2,000 pounds concentrated for heavy-duty models) with ¼ inch deflection.

1.07 QUALITY ASSURANCE

A. Manufacturer: Obtain [trench cover]  [access cover] assemblies through one source from a single manufacturer.

1. Manufacturer shall have a minimum of ten (10) years of experience in the fabrication of [trench cover] [access cover] [trench liner] assemblies.

B. Installer: Firm with not less than three (3) years of successful experience in the installation of systems similar to those required by this project and acceptable to the manufacturer of the system.

1.08 SUBMITTALS

A. Submission must be made within ten (10) working days of the General Contract award to avoid project delay.  If not adhered to, the Architect will designate the exact product to be used, and the contractor will have no recourse.

- Submit manufacturer’s specifications and technical data, including Material Safety Data Sheets, installation instructions, and, as required, catalog cuts and templates explaining construction and providing for incorporation of the product into the project.

- Submit shop drawings showing complete fabrication details for all [trench covers] [access covers] [trench liners], including required anchorage to surrounding construction, recesses, blocking, and connections between similar and dissimilar trench cover assemblies.

1.09 DELIVERY, STORAGE AND HANDLING

- Provide temporary protective cover on [anodized aluminum] [stainless steel] [bronze] finished surfaces.

- Deliver [trench covers] [access covers] [trench liner] to jobsite in new, clean, unopened crates of sufficient size and strength to protect materials during transit.

- Store components in original containers in a clean, dry location.

- Handle components with equipment of sufficient size to preclude hazard to personnel or damage to components.

1.10 WARRANTY

A. Submit manufacturer’s warranty that materials furnished will perform as specified for a period of not less than one (1) year when installed in accordance with manufacturer’s recommendations.

PART 2 — PRODUCTS

2.01 ACCEPTABLE MANUFACTURERS

- Furnish and install as noted in specifications and as indicated on drawings, [Trench cover (type no.)] [Access cover (type no.)] [Trench liners] as manufactured by: MM Systems Corporation, 50 MM Way, Pendergrass, GA. 30567; phone: 800-241-3460 or (706) 824-7500; fax: (706) 824-7501.

- The products herein specified are [standard] [custom] manufactured products of the listed manufacturer.

- Substitutions:  Submit proposed substitutions in writing to Architect no less than 10 days before bids are due.  Submit samples and product data to demonstrate acceptability of proposed substitute.  Acceptance will be by Addendum.

2.02 MATERIALS

[A.] [Trench Covers shall be aluminum, ASTM B 209, alloy 6061-T6 for plate; Frames shall be aluminum, ASTM B221, alloy 6063-T5 for extrusions.]

[B.] [Access Covers shall be aluminum, ASTM B 209, alloy 6061-T6 for plate; frames shall be aluminum, ASTM B 221, alloy 6063-T5 for extrusions.]

C. Trench liners:  [Manufacturer and type number].

1. Galvanized Steel:  ASTM A 653, G90, [20 gauge] [_______ gauge].

2. Aluminum:  ASTM B 209, alloy 5052–H32, [0.063”] [_______].

3. Stainless Steel: ASTM A 666, type 304, [22 gauge] [_______ gauge].

- Abrasive: Two (2) part Epoxy combined with aluminum oxide grit.

- Fasteners, accessories, and other materials required for complete installation to manufacturer's instructions.

2.03 FABRICATION

- Fabricate [trench cover] [access cover] [trench liner] assemblies as detailed.

- Fabricate [trench covers] [access covers] of [__________] length and [__________] width.

- Fabricate trench liner of  [__________] length, [__________] width, and [__________] depth.

- Fabricate splices, special transitions, corner units, corner fittings, intersections, and end closures as required.

- Miter and weld joints shall be factory manufactured.

- Provide necessary and related parts, devices, anchors, and other items required for water-resistant installations.

B. [Trench covers] [Access covers] shall have a [plain] [abrasive] [diamond tread] [1/8 inch recessed] [perforated] surface.

2.04 FINISHES

A. Aluminum:

- Exposed aluminum surfaces shall be [mill finish] [anodized finish selected].

- Abrasive:  Abrasive available in colors.

PART 3 — EXECUTION

3.01 EXAMINATION

A. Contractor shall verify that field measurements [and blockout dimensions] are as shown on shop drawings prior to releasing materials for fabrication by the manufacturer.

B. Installer shall examine conditions under which work is to be performed and shall notify the contractor in writing of unsatisfactory conditions. Installer shall not proceed until unsatisfactory conditions have been corrected in a manner acceptable to the installer.

3.02 INSTALLATION

A. Install [trench covers] [access covers] [trench liners] in accordance with the manufacturer’s written installation instructions.  Anchor spacing shall be in accordance with approved shop drawings.

B. Align work plumb, level, and, as required, flush with adjacent surfaces.

C. Make allowances for change in trench size due to difference between installation and existing building construction.

  - CLEANING

A. Clean exposed surfaces as recommended by the manufacturer.

3.04 ADJUSTING AND PROTECTION

A. Inspect system components for proper fit.  Adjust, repair or replace components not conforming to requirements. Repair or replacement of an individual unit shall be as approved by the Architect.

- Finished units shall be without damage. Units damaged during shipping or construction shall be repaired by the contractor at the expense of the party damaging the material, in accordance with the contract requirements.

- Protect installation from damage by work of other Sections.  Where required, remove and store [trench covers] [access covers] and install temporary protection over trench; re-install [trench covers] [access covers] prior to Substantial Completion of the work.

3.05 GENERAL RESPONSIBILITY

A. Any variation from this specification resulting in additional cost to any other contractor or subcontractor on this project shall be the sole financial responsibility of the contractor for the work of this section.

3.06 SCHEDULE

- Indicate MM Systems Corporation product number on Drawings or Schedule.

- Interior Trench Cover: __________

- Exterior Trench Cover: __________

- Interior Access Cover: __________

- Exterior Access Cover: __________

- Interior Trench Liner: __________

- Exterior Trench Liner: __________